## Slide 1: Notes: ECU LIVE RAM Write rev 1.0

## Slide 2: USB Interface v2
Purchased VID/PID: 0x16D0 / 0x05A3
* ECU -> PC GetReport() reports (HID_REPORT_ITEM_In)
* HID_REPORT_ID_DEBUG
* HID_REPORT_ID_DIAG_STATUS
* HID_REPORT_ID_MCU_STATUS
* HID_REPORT_ID_DIAG
* HID_REPORT_ID_FLASH_READ
* HID_REPORT_ID_EEPROM_READ
* HID_REPORT_ID_RAM_STATUS
* HID_REPORT_ID_ABOUT
* ECU -> PC GetFeature() reports (HID_REPORT_ITEM_Feature)
* HID_REPORT_ID_MCU_CONTROL
* HID_REPORT_ID_DIAG_CONTROL
* HID_REPORT_ID_DEBUG_CONTROL
* HID_REPORT_ID_MODE_CONTROL
* PC -> ECU SetReport() reports (HID_REPORT_ITEM_Out)
* HID_REPORT_ID_FLASH_SET_ADDRESS
* HID_REPORT_ID_FLASH_WRITE
* HID_REPORT_ID_EEPROM_SET_ADDRESS
* HID_REPORT_ID_EEPROM_WRITE
* HID_REPORT_ID_RAM_WRITE
* PC -> ECU SetFeature() reports (HID_REPORT_ITEM_Feature)
* HID_REPORT_ID_MCU_CONTROL
* HID_REPORT_ID_DIAG_CONTROL
* HID_REPORT_ID_MODE_CONTROL
* HID_REPORT_ID_DEBUG_CONTROL

## Slide 3
HID_REPORT_ID_RAM_STATUS (0x87)
Resume 1 bit flag to request use of previous address+1
Reserved 5 bits unused
Mcu 2 bits MCU number
Address 16 bit DENSO address space to write to
Status Status byte
Summary Input Reports (ECU → PC)
/* RAM write status input report */
#define HID_REPORT_ID_RAM_STATUS (0x87)
typedef struct
{
uint8_t Resume:1;
uint8_t Reserved:5;
uint8_t Mcu:2;
uint16_t Address;
uint8_t Status;
} ATTR_PACKED HID_Report_Ram_Status_t;

## Slide 4
HID_REPORT_ID_RAM_WRITE (0x86)
Resume 1 bit flag to request use of previous address+1
Reserved 5 bits unused
Mcu 2 bits MCU number
Address 16 bit DENSO address location (64kB max), ignored if resume=true
DataNumEntries number of entries in data byte array (max DIAG_RAM_SIZE)
Data[DIAG_RAM_SIZE] byte array of data to write to DENSO sram starting at specified Address
Summary Output Reports (PC → ECU)
/* RAM write output report */
#define HID_REPORT_ID_RAM_WRITE (0x86)
typedef struct
{
uint8_t Resume:1;
uint8_t Reserved:5;
uint8_t Mcu:2;
uint16_t Address;
uint8_tDataNumEntries;
uint8_t Data[DIAG_RAM_SIZE];
} ATTR_PACKED HID_Report_Ram_Write_t;

## Slide 5
Program Flow
Get status report and verify status is RAM_RDY getReport(HID_REPORT_ID_RAM_STATUS, reportRamStatus, sizeof(reportRamStatus)) reportRamStatus.Status, 0 = RAM_OFF (hardware does not support live writing to RAM) 1 = RAM_RDY (ready for live RAM write) 2 = RAM_DATA (data queued for writing, typically this means the ECU is not running, but it could also mean the data is still in the process of being written)
Load the report structure as follows reportRamWrite.Resume = false; (false to write to specified address, true to use last address written +1, uses less overhead) reportRamWrite.Mcu = Mcu; select MCU to write to reportRamWrite.Address = LiveAddress; 16bit Denso starting address for data array (not used if Resume=true) reportRamWrite.DataNumEntries = n; data array contains n bytes reportRamWrite.Data[index] = datum_idx; data byte for specified array element
Write report to AVR setReport(HID_REPORT_ID_RAM_WRITE, reportRamWrite, (sizeof(reportRamWrite)))
Check status report for errors getReport(HID_REPORT_ID_RAM_STATUS, reportRamStatus, sizeof(reportRamStatus))
Interrogate status report for RAM_OK to confirm write completed successfully
reportRamStatus.Mcu selected Mcu for write
reportRamStatus.Resume, false=using address specified, true= resume writing from last address+1 reportRamStatus.Status, 0 = RAM_OFF (hardware does not support live writing to RAM)
1= RAM_RDY ready for live RAM write)
2=RAM_DATA (data queued for writing, typically this means the ECU is not running, but it could also mean the data is still in the process of being written)
3=RAM_OK Data written successfully to MCU
4=RAM_ERR Data write failed. Usually because MCU code does not exist to handle live write, or ECU powered down during write.
reportRamStatus.Address starting address used for data array ram write (not meaningful if resume=true)
Live Write Prototype Code

## Slide 6: AVR-MCU RAM Write Operation
Writing address 0x32 (with starting address) or 0x43 (resume write using last address + 1) to the diagnostics interface initiates the RAM writing operation. Note: 3S style ECUs use 0x19 and 0x1A to initiate writes.
Process is as follows:
send 0x32
ecu acks 0x32 then ECU waits for next byte
send address MSB
ecu acks MSB then ECU waits for next byte
send address LSB
ecu acks LSB then ECU waits for next byte
send data byte
ecu acks byte then ECU waits for next byte, unless bit9 set on previous data byte
Done
Process is as follows for resume write:
send 0x34
ecu acks 0x34 then ECU waits for next byte
send data byte
ecu acks byte then ECU waits for next byte, unless bit9 set on previous data byte
Done
Timing
The first write with a specified address takes 4 ADC cycles. Each additional data byte adds one more ADC cycle, so the formula is
  T = (3 + n)Tadc where Tadc is the ADC conversion rate (~5ms for 7M) and n is the number of data bytes (1-32)
For a resume write, where the address is inherited, the formula changes to
    T = (1 + n)Tadc where Tadc is the ADC conversion rate (~5ms for 7M)
ADC States consumed:.
After each acknowledgement byte from the ECU, the ECU exits the ADC interrupt.
If no data is received on the next ADC interrupt, the ECU declares a timeout error and the write process is cancelled and the mode is set back to diagnostics.

## Slide 7: AVR-MCU 16 bit interface
ECU sends sync byte (value depends on ECU mode)
AVR responds with 16 bit command or data. A command is indicated by values in the 0x1000 to 0x10FF range.
ECU responds with 16 bit acknowledgement or data.
Commands:
0x00DA – Switch to diagnostic read mode
0x00DB – Switch to diagnostic write mode (16 bit writes) with address
0x00DC – Switch to diagnostic write mode (16 bit writes) continue with previous address
0x00DD – Switch to diagnostic write mode (8 bit writes) with address
0x00DE – Switch to diagnostic write mode (8 bit writes) continue with previous address
Modes:
0xDA – Diagnostic Read Mode
0xDB – Diagnostic Write Mode (16 bit), Address
0xDC – Diagnostic Write Mode (16 bit), Data
0xDD – Diagnostic Write Mode (8 bit), Address
0xDE – Diagnostic Write Mode (8 bit), Data
Command/Data
Ack/Data
Sync
MSB
LSB
MSB
LSB
ECU
AVR
Time
1
0

## Slide 8: AVR-MCU RAM Read with 16 bit interface
ECU starts in diagnostic mode, so sync byte is 0xDA
AVR responds with 16 bit address to be read
ECU reads memory at address and sends 16 bit value in response.
Address
Data
DA
ADR MSB
ADR LSB
Data MSB
Data LSB
ECU
AVR
Time
0
0

## Slide 9: AVR-MCU RAM Write with 16 bit interface
ECU starts in diagnostic mode, so sync byte is 0xDA
AVR responds with 16 bit command 0x00DB to switch into write mode (16 bit).
ECU sends 16 bit acknowledgement of 0x00DB
After 4ms, ECU sends sync byte of 0xDB to indicate address phase of write mode
AVR responds with 16 bit address
ECU echoes back address
After 4ms, ECU sends sync byte of 0xDC to indicate data phase of write mode
AVR responds with 16 bit value to write
ECU writes to RAM and echoes back data
To exit diagnostic write mode, the AVR can write a new command.
Command
Acknowledgment
DA
00
DB
00
DB
ECU
AVR
Time
DB
ADR MSB
ADR LSB
ADR MSB
ADR LSB
Address
Acknowledgment
DC
Data MSB
Data LSB
Data MSB
Data LSB
16-Bit Data
Acknowledgment
0
1
0
0
0
0

## Slide 10: AVR-MCU RAM Write with 16 bit interface
ECU starts in diagnostic mode, so sync byte is 0xDA
AVR responds with 16 bit command 0x00DD to switch into write mode (8 bit).
ECU sends 16 bit acknowledgement of 0x00DD
After 4ms, ECU sends sync byte of 0xDD to indicate address phase of write mode
AVR responds with 16 bit address
ECU echoes back address
After 4ms, ECU sends sync byte of 0xDE to indicate data phase of write mode
AVR responds with 16 bit value, 8 bit value to write is in MSB, LSB is ignored
ECU writes to RAM and echoes back 8 bit value in both MSB and LSB.
To exit diagnostic write mode, the AVR can write a new command.
Command
Acknowledgment
DA
00
DD
00
DD
ECU
AVR
Time
DD
ADR MSB
ADR LSB
ADR MSB
ADR LSB
Address
Acknowledgment
DE
Data MSB
Don’t Care
Data MSB
Data LSB
8-Bit Data
Acknowledgment
0
1
0
0
0
0

## Slide 11: Notes: Toyotune/GF Flash/SRAM Manipulation rev 1.0

## Slide 12: USB Interface v2
Purchased VID/PID: 0x16D0 / 0x05A3
* ECU -> PC GetReport() reports (HID_REPORT_ITEM_In)
* HID_REPORT_ID_DEBUG
* HID_REPORT_ID_DIAG_STATUS
* HID_REPORT_ID_MCU_STATUS
* HID_REPORT_ID_DIAG
* HID_REPORT_ID_FLASH_READ
* HID_REPORT_ID_EEPROM_READ
* HID_REPORT_ID_RAM_STATUS
* HID_REPORT_ID_ABOUT
* ECU -> PC GetFeature() reports (HID_REPORT_ITEM_Feature)
* HID_REPORT_ID_MCU_CONTROL
* HID_REPORT_ID_DIAG_CONTROL
* HID_REPORT_ID_DEBUG_CONTROL
* HID_REPORT_ID_MODE_CONTROL
* PC -> ECU SetReport() reports (HID_REPORT_ITEM_Out)
* HID_REPORT_ID_FLASH_SET_ADDRESS
* HID_REPORT_ID_FLASH_WRITE
* HID_REPORT_ID_EEPROM_SET_ADDRESS
* HID_REPORT_ID_EEPROM_WRITE
* HID_REPORT_ID_RAM_WRITE
* PC -> ECU SetFeature() reports (HID_REPORT_ITEM_Feature)
* HID_REPORT_ID_MCU_CONTROL
* HID_REPORT_ID_DIAG_CONTROL
* HID_REPORT_ID_MODE_CONTROL
* HID_REPORT_ID_DEBUG_CONTROL

## Slide 13
The memory operation is primarily controlled by the FLASH_SET_ADDRESS report as detailed below.
HID_REPORT_ID_FLASH_SET_ADDRESS (0x80)
Select 6 bit memory operation selector defined as:
MEMORY_SEL_FLASH (0x00) memory read/write 0 to 32 bytes of data to flash
MEMORY_SEL_SRAM (0x01) memory read/write 0 to 32 bytes of data to SRAM
MEMORY_SEL_ERASE (0x02) memory erase flash 4kB sector
MEMORY_SEL_CPFS (0x03) block memory copy specified flash page to 8kB of SRAM
MEMORY_SEL_CPSF (0x04) block memory copy 8kB SRAM to specified flash page(s)
Mcu 2 bit MCU number
Address 27bit AVR address location (0 to 128MB)
for MEMORY_SEL_FLASH/ MEMORY_SEL_SRAM address is start of data write/read for MEMORY_SEL_ERASE, address is start of sector (i..e Address & 0x7FFF000) for MEMORY_SEL_CPFS, address is flash page number (0-0xFF). Note: Gapfiller uses two 4-bit pages mux’d together for MEMORY_SEL_CPSF, address is flash page number (0-0xFF). Note: Gapfiller uses two 4-bit pages mux’d together
NumBytes 5 bit number of entries in data byte array (1 to 32 bytes) use 0 for MEMORY_SEL_ERASE, MEMORY_SEL_CPFS, MEMORY_SEL_CPSF
Summary Output Reports (PC → ECU)
/* Flash set address output report */
#define HID_REPORT_ID_FLASH_SET_ADDRESS (0x80)
typedef struct
{
uint8_t Select:6;
uint8_t Mcu:2;
uint32_t Address:27;
uint32_t NumBytes:5;
} ATTR_PACKED HID_Report_Flash_Set_Address_t;

## Slide 14
Program Flow (example write to SRAM)
Check and/or set AVR to Programming Mode reportModeControl.Mode = MODE_PROGRAM; setFeature(HID_REPORT_ID_MODE_CONTROL, reportModeControl, HID_REPORT_SIZE(HID_Report_Mode_Control))
Load the report to specify memory mode selection and address, number of bytes, mcu FlashSetAddressReport->Mcu = (uint8_t) Mcu & 0x3; FlashSetAddressReport->NumBytes = (uint8_t) NumBytes & 0x1F; FlashSetAddressReport->Address = Address & 0x7FFFFFF; FlashSetAddressReport->Select = MEMORY_SEL_SRAM;
Write address report to AVR setReport(HID_REPORT_ID_FLASH_SET_ADDRESS, FlashSetAddressReport, HID_REPORT_SIZE(HID_Report_Flash_Set_Address))
Load report with data FlashWriteReport->Data[index] = Data[index]
Write data report to AVR
setReport(HID_REPORT_ID_FLASH_WRITE, FlashWriteReport, HID_REPORT_SIZE(HID_Report_Flash_Write))
See toyotune_cmd_win32 project for more examples
GF/Toyotune Memory Prototype Code